## Slide 1
Environment
Economics
Equity

## Slide 3: Technical Architecture
(3) Ovens Electricity Data
Current, Volts
Utility Bills (PDF)
Monthly
Incoming Electricity Data
30 min. increments
NOAA Weather Data
Barcode Scanner Data for Ovens
1 unit per cycle
Air Compressor Data
15 min increments
Headless CMS
Dashboard
Tabula
+ CRON
REST API
Opens Opportunity for external Integration
RNN Predictive Model
Mean Absolute percentage Error (mape) 4.868%
Relay Control or PLC to Switch/Add Battery Power Automatically
MS Azure + Databricks for Model Development
Github – Source Control + Collaboration
VS Code
Excel
Tools
Notes: Noel
Let’s begin with discussing the data you have available. First, you will have data regarding the incoming electricity to the plant in 30 minutes intervals. This is provided by our utility company. From the utility bills, we can derive a 'blended rate' for the cost of energy consumed – given all of the variable billing components and the total energy consumed, what was the final cost per kWh?
We also have energy data from a handful of machines: an air compressor, and three ovens. Given the blended energy cost rate, we can calculate a rough approximation of the cost of the energy consumed by those machines during the billing cycle covered by the bill.
We also have data from a barcode scanner, which tells us when items enter the oven. This data will give us insight into the energy profile of the machine when units enter the oven versus when they are not entering the oven. This will enable you to determine the state of each piece of equipment, while also understanding it’s OEEE.
From there, you will analyze the data with additional data sources (like the utility bills we provided and additional 3rd party data not provided, such as weather data for calculating heating and cooling degree days) to create real-time—and forecasted—cost and emissions insights. The results of your findings will then be displayed on an intuitive dashboard sharing real-time present and forecasted insights.

## Slide 4: Dashboard

## Slide 5: Dashboard
Easy
Streamlined
Powerful

## Slide 6: Charts

## Slide 7: Equipment Monitoring

## Slide 8: Data Analysis

## Slide 9: Understanding the Challenge and Data
Utilities Perspective
Used Python/Tabula to Convert PDF to CSV for July 20 Usage Statement –
Clean up using Excel – Fix Dates, Format
Possible Connection Between Average Day Cost Per Month & The Average Temperature Per Month

## Slide 11: Productivity of SM4 Oven for July 2020​
Showing Productivity 11- 25 ​

## Slide 12: Data Analysis

## Slide 13: Understanding data (July)
The file provides data for energy usage of three ovens (SM1, SM4, SM7):
Average current per 15 min
Average voltage per 15 min
Extract Energy
= V *I*t

## Slide 14: Variables used in model development
The file provides per min data of:

## Slide 15: Prediction
The file provides Information about the three ovens (SM1, SM4, SM7)

## Slide 16: Training an RNN (LSTM) model
Model features

## Slide 17
Headless CMS Admin Inerface

## Slide 18: Thank You